Software description

1. MCU resources utilization

Software based on 3 semi-independent processes:
a) data acquisition, filtering and calculation of parameters;
b) calculated data and runtime parameters interchange processing;
c) modbus slave transaction processing.

Section A tasks computing as SysTick interrupt-bases state machine, main sync-cycle is equal of data acquisition period.

Section B tasks – is a main infinite loop (lowest priority), which waits modbus transaction and sent appropriate data to maser.

Section C task – is modbus RTU slave driver, based on UART and TIM7 interrupts.

2. State machine description

State machine of HM soft consist of 3 global state:
a) Idle state (for setup of system settings or maintenance);
b) Measuring mode (normal cyclic measuring);
c) Calibration mode (time-limit measuring with special parameters).

2.1 Measuring mode state machine